## Slide 1
Ships Synoptic Code and Observing Methods
THE SHIPS SYNOPTIC CODE FM13-X
Code FM-13-X-SHIP, the ships synoptic code, is contained of 23 groups of symbolic letters representing meteorological and oceanographic elements, report identification and ship location data.
BBXX D.....D YYGGiw 99LaLaLa QcLoLoLoLo iRixhVV Nddff 00fff 1snTTT 2snTdTdTd 4PPPP 5appp 7wwW1W2 8NhCLCMCH 222Dsvs 0ssTwTwTw 2PwPwHwHw 3dw1dw1dw2dw2 4Pw1Pw1Hw1Hw1 5Pw2Pw2Hw2Hw2 6IsEsEsRs 8swTbTbTb ICE ciSibiDizi (or plain language)

## Slide 2
The ship synoptic code has three main sections 0, 1, and 2.
Section 0, consisting of the first 5 code groups,
Contains the identification data (ship report identifier, ship’s call sign, date, time, location), and units of wind speed used.
Ships Synoptic Code Section 0
Cont’d

## Slide 3
Section 1 consists of code groups 6-14 and contains most of the meteorological data of the report (precipitation and weather data indicators, cloud base height, visibility, cloud cover, wind direction and speed, air and dew point temperatures, sea level pressure, the 3 hours pressure change and tendency character, present and past weather, and cloud type).
Ships Synoptic Code Section 1
Cont’d
iRixhVV Nddff 00fff 1snTTT 2snTdTdTd
4PPPP 5appp 7wwW1W2 8NhCLCMCH

## Slide 4
Section 2 consists of code groups 15-23 and contains ships movement data (ships course and speed), oceanographic data (sea surface temperature, wind wave period and height, primary and secondary swell direction, period, and height), and ice data (for any ice deposit on ship or on the sea surface), and the wet-bulb temperature group.
Ships Synoptic Code Section 2
Cont’d
222Dsvs 0ssTwTwTw 2PwPwHwHw 3dw1dw1dw2dw2 4Pw1Pw1Hw1Hw1 5Pw2Pw2Hw2Hw2 6IsEsEsRs 8swTbTbTb ICE ciSibiDizi

## Slide 5
Cont’d
BBXX, Ship Report Indicator
SECTION 0 — IDENTIFICATION DATA
BBXX D.....D YYGGiw 99LaLaLa QcLoLoLoLo
SECTION 1 — METEOROLOGICAL DATA
iRixhVV Nddff 00fff 1snTTT 2snTdTdTd
4PPPP 5appp 7wwW1W2 8NhCLCMCH
SECTION 2 — OCEANOGRAPHIC DATA
222Dsvs 0ssTwTwTw 2PwPwHwHw 3dw1dw1dw2dw2 4Pw1Pw1Hw1Hw1 5Pw2Pw2Hw2Hw2 6IsEsEsRs 8swTbTbTb ICE ciSibiDizi
Definition: The symbolic letters BBXX identify a ship report from a sea station.

## Slide 6
The identification of stations located at sea on a drilling rig or an oil- or gas-production platform shall be indicated by the group A1bwnbnbnb.
Cont’d
D . . . . D, Ship’s Radio Call Sign
SECTION 0 — IDENTIFICATION DATA
BBXX D.....D YYGGiw 99LaLaLa QcLoLoLoLo
SECTION 1 — METEOROLOGICAL DATA
iRixhVV Nddff 00fff 1snTTT 2snTdTdTd 4PPPP 5appp 7wwW1W2 8NhCLCMCH
SECTION 2 — OCEANOGRAPHIC DATA
222Dsvs 0ssTwTwTw 2PwPwHwHw 3dw1dw1dw2dw2 4Pw1Pw1Hw1Hw1 5Pw2Pw2Hw2Hw2 6IsEsEsRs 8swTbTbTb ICE ciSibiDizi
D.....D - Ship’s call sign consisting of three or more alphanumeric characters.

## Slide 7
SECTION 0 — IDENTIFICATION DATA
BBXX D.....D YYGGiw 99LaLaLa QcLoLoLoLo
SECTION 1 — METEOROLOGICAL DATA
iRixhVV Nddff 00fff 1snTTT 2snTdTdTd
4PPPP 5appp 7wwW1W2 8NhCLCMCH
SECTION 2 — OCEANOGRAPHIC DATA
222Dsvs 0ssTwTwTw 2PwPwHwHw 3dw1dw1dw2dw2 4Pw1Pw1Hw1Hw1 5Pw2Pw2Hw2Hw2 6IsEsEsRs 8swTbTbTb ICE ciSibiDizi
YYGGiw Day of the Month, Actual Time of Observation to the Nearest Whole Hour and Wind Speed Indicator
Definition: YY - Day of the month (UTC) Universal Time Coordinated, not by local date or time.
GG - The actual time of observation (UTC) rounded to the nearest whole hour UTC.
Note: Observations should be submitted no more than 29 minutes prior to, or 29 minutes after the synoptic hour.
iw - Indicator for source and units of wind speed. Source is how the measurement was made (either estimated or measured). Units: Knots.

## Slide 8
Ship position indicator group
99LaLaLa QcLoLoLoLo
Section 0 — Identification data
BBXX D.....D YYGGiw 99LaLaLa QcLoLoLoLo
Section 1 — Meteorological data
iRixhVV Nddff 00fff 1snTTT 2snTdTdTd
4PPPP 5appp 7wwW1W2 8NhCLCMCH
Section 2 — Oceanographic data
222Dsvs 0ssTwTwTw 2PwPwHwHw 3dw1dw1dw2dw2 4Pw1Pw1Hw1Hw1 5Pw2Pw2Hw2Hw2 6IsEsEsRs 8swTbTbTb ICE ciSibiDizi
99 ship position group indicator
LaLaLa - Ship’s latitude, in degrees and tenths of a degree, measured in terms of degrees north or south of the equator.
Qc - Quadrant of the globe. Varies according to Ship’s position with respect to the equator (0˚ latitude) and the Greenwich Meridian (0˚ longitude).
LoLoLoLo Ship’s longitude, in degrees and tenths of a degree, measured in terms of degrees north or south of the equator.

## Slide 9
Cont’d
Method of Measurement Latitude:
Determine latitude using standard shipboard methods. Tenths is obtained by dividing the number of minutes by 6, and disregarding the remainder. Ignore seconds.
How to Code Latitude:
    Always coded with three digits, the first two digits are actual degrees, the last digit for tenths of a degree. For example when ship’s position lat. 46˚ 41’ 23’’ it is coded as (46˚ is coded as it is, 41’ divided by 6 is 6.833, .833 is disregarded and 23’’ become ignored) =466;
    In the case of Qc If the ship in north of the equator (north latitude), Qc is coded as 1 when east of the Greenwich Meridian (east longitude), or as 7 when west of the Greenwich meridian; If the ship in south of the equator (south latitude), Qc is coded as 3 when east of the Greenwich meridian, or as 5 when west of the Greenwich meridian.

## Slide 10
How to Code Longitude:
Always coded with four digits, with the leading (hundreds) figure coded as 0 or 1.
The first three digits are actual degrees, the last digit for tenths of a degree. For example:-
    when ship’s position Lon. 142˚ 55’ 30’’ it is coded as (142˚ is coded as is, 55’ divided by 6 is 9.166, .166 is disregarded we take 9 only and 30’’ become ignored) =1429;
    when ship’s position Lon. 60˚ 35’ 50’’ it is coded as (60˚ is coded as 060, 35 divided by 6 = 5.833, .833 is disregarded we take 5 only and 50’’ become ignored) LoLoLoLo = 0605;

## Slide 11
iRixhVV
Section 0 — Identification data
BBXX D.....D YYGGiw 99LaLaLa QcLoLoLoLo
Section 1 — Meteorological data
iRixhVV Nddff 00fff 1snTTT 2snTdTdTd 4PPPP 5appp 7wwW1W2 8NhCLCMCH
Section 2 — Oceanographic data
222Dsvs 0ssTwTwTw 2PwPwHwHw 3dw1dw1dw2dw2 4Pw1Pw1Hw1Hw1 5Pw2Pw2Hw2Hw2 6IsEsEsRs 8swTbTbTb ICE ciSibiDizi
iR - Indicator for Inclusion or Omission of Precipitation (4)
How to Code: Always coded as 4 for U.S. VOS program ships. This indicates that the precipitation group is omitted.
ix - Is coded as 1 or 3

## Slide 12
VV - Visibility is the greatest distance an object can be seen and identified.
The visibility ranges corresponding to various weather types are as follows:
Code fig. | Visibility in m/km
90 | less than 50 m
91 | 50 but less than 200 m
92 | 200 but less than 500 m
93 | 500 but less than 1000 m
94 | 1 but less than 2 km
95 | 2 but less than 4 km
96 | 4 but less than 10 km
97 | 10 but less than 20 km
98 | 20 but less than 50 km
99 | 50 km or more

## Slide 13
Section 0 — Identification data
BBXX D.....D YYGGiw 99LaLaLa QcLoLoLoLo
Section 1 — Meteorological data
iRixhVV Nddff 00fff 1snTTT 2snTdTdTd 4PPPP 5appp 7wwW1W2 8NhCLCMCH
Section 2 — Oceanographic data
222Dsvs 0ssTwTwTw 2PwPwHwHw 3dw1dw1dw2dw2 4Pw1Pw1Hw1Hw1 5Pw2Pw2Hw2Hw2 6IsEsEsRs 8swTbTbTb ICE ciSibiDizi
Code procedure of Oceanographic data
222Dsvs
2 2 2 - Section indicator for maritime data
Ds Ship's course made good during the past 3 hours
Units: Compass directions.
Code Figures (DS) | True Direction
0 | Ship hove to
1 | NE
2 | E
3 | SE
4 | S
5 | SW
6 | W
7 | NW
8 | N
9 | Unknown
/ | Not reported

## Slide 14
Vs - Ship's average speed during the past 3 hours
Units: Knots.
Code Figures(Vs) | Average speed (knots) | Average speed (km/hrs)
0 | 0 knot | 0 km h–1
1 | 1 to 5 knots | 1-10 km h-1
2 | 6 to 10 knots | 11-19 km h-1
3 | 11 to 15 knots | 20-28 km h-1
4 | 16 to 20 knots | 29-37 km h-1
5 | 21 to 25 knots | 38-47 km h-1
6 | 26 to 30 knots | 48-56 km h-1
7 | 31 to 35 knots | 57-65 km h-1
8 | 36 to 40 knots | 66-75 km h -1
9 | Over 40 knots | Over 75 km h-1
/ | Not applicable (report from a coastal land station) or not reported | 

## Slide 15
Section 0 — Identification data
BBXX D.....D YYGGiw 99LaLaLa QcLoLoLoLo
Section 1 — Meteorological data
iRixhVV Nddff 00fff 1snTTT 2snTdTdTd 4PPPP 5appp 7wwW1W2 8NhCLCMCH
Section 2 — Oceanographic data
222Dsvs 0ssTwTwTw 2PwPwHwHw 3dw1dw1dw2dw2 4Pw1Pw1Hw1Hw1 5Pw2Pw2Hw2Hw2 6IsEsEsRs 8swTbTbTb ICE ciSibiDizi
0ssTwTwTw : 0 - Group indicator for sea surface temperature ss - Sign and type of measurement of sea surface temperature TwTwTw - Sea surface temperature in whole degrees and tenths

## Slide 16
Coding procedure for ss - Sign and type of measurement of sea surface temperature
Method of Measurement:
    Engine room intake thermometer,
    hull mounted contact sensor thermometer,
    bucket thermometer.

## Slide 17
2PwPwHwHw wind wave period and height
SECTION 2 — OCEANOGRAPHIC DATA
222Dsvs 0ssTwTwTw 2PwPwHwHw 3dw1dw1dw2dw2 4Pw1Pw1Hw1Hw1 5Pw2Pw2Hw2Hw2 6IsEsEsRs 8swTbTbTb ICE ciSibiDizi
2PwPwHwHw :
2 - Group indicator for wind waves.
PwPw - Period of wind waves in seconds.
Wave period is the time between the passage of two successive wave crests (or successive troughs) and Units: Seconds.
HwHw - The vertical distance between trough and crest for wind waves in units of half meter .

## Slide 18
Cont’d
Method of Measurement:
Visual estimate.
How to Code:
The code is in units of half meters e.g. code figure 08 is 8 half meters = 4 meters = 13 feet:

## Slide 19
SECTION 2 — OCEANOGRAPHIC DATA
222Dsvs 0ssTwTwTw 2PwPwHwHw 3dw1dw1dw2dw2 4Pw1Pw1Hw1Hw1 5Pw2Pw2Hw2Hw2 6IsEsEsRs 8swTbTbTb ICE ciSibiDizi
3dw1dw1dw2dw2 swell directions
3dw1dw1dw2dw2
  3 - Group indicator for swell directions
  dw1dw1 - Direction in tens of degree from which the predominant swell is coming
  dw2dw2 Direction of secondary Swell Waves in degrees.

## Slide 20
4Pw1Pw1Hw1Hw1 period and height of the predominant swell
Section 2 — Oceanographic data
222Dsvs 0ssTwTwTw 2PwPwHwHw 3dw1dw1dw2dw2 4Pw1Pw1Hw1Hw1 5Pw2Pw2Hw2Hw2 6IsEsEsRs 8swTbTbTb ICE ciSibiDizi
4Pw1Pw1Hw1Hw1
4 - Group indicator
Pw1Pw1 - Period of the first (predominant) swell in seconds
Hw1Hw1 - Height of the first (predominant) swell in units of half meter
How to Code: for Pw1Pw1 Coded directly in seconds. Thus, if the period of the primary swell waves is 12 seconds, Pw1Pw1 is coded as 12. If the period is 7 seconds, Pw1Pw1 is coded as 07.

## Slide 21
5Pw2Pw2Hw2Hw2 Secondary Swell Waves Period and height
Section 2 — Oceanographic data
222Dsvs 0ssTwTwTw 2PwPwHwHw 3dw1dw1dw2dw2 4Pw1Pw1Hw1Hw1 5Pw2Pw2Hw2Hw2 6IsEsEsRs 8swTbTbTb ICE ciSibiDizi
5Pw2Pw2Hw2Hw2
5 - Group indicator
Pw2Pw2 - Period of Secondary Swell Waves (Units: Seconds).
Hw2Hw2 - Height of secondary swell waves, in units of half meter.
The secondary swell system has lower waves than the primary swell.

## Slide 22
6IsEsEsRs - ice deposit on ship
Section 2 — Oceanographic data
222Dsvs 0ssTwTwTw 2PwPwHwHw 3dw1dw1dw2dw2 4Pw1Pw1Hw1Hw1 5Pw2Pw2Hw2Hw2 6IsEsEsRs 8swTbTbTb ICE ciSibiDizi
6IsEsEsRs
6 - Group indicator
Is, Cause of Ice Deposit on Ship
EsEs, Thickness of Ice Deposit on Ships
Rs, Rate of Ice Deposit on Ships

## Slide 24
8swTbTbTb - Wet Bulb Temperature
Section 2 — Oceanographic data
222Dsvs 0ssTwTwTw 2PwPwHwHw 3dw1dw1dw2dw2 4Pw1Pw1Hw1Hw1 5Pw2Pw2Hw2Hw2 6IsEsEsRs 8swTbTbTb ICE ciSibiDizi
8swTbTbTb
8 - Group indicator for wet bulb temperature
sw - Sign and type of wet bulb temperature
TbTbTb - Wet bulb temperature in whole degrees and tenths

## Slide 25
ICE ciSibiDizi - Concentration or arrangement of sea ice
Section 2 — Oceanographic data
222Dsvs 0ssTwTwTw 2PwPwHwHw 3dw1dw1dw2dw2 4Pw1Pw1Hw1Hw1 5Pw2Pw2Hw2Hw2 6IsEsEsRs 8swTbTbTb ICE ciSibiDizi
ICE ciSibiDizi
ICE, Indicator for Sea Ice Concentration
Method of Measurement: Visual determination.
How to Code: Code in accordance with the table on the following
ci Sea ice concentration 0-9, /
Si Sea ice development 0-9, /
bi Ice of land origin 0-9, /
Di Ice edge bearing 0-9, /
zi Ice trend 0-9, /