## Slide 1
FM 35–XI Ext. TEMP - Upper-level pressure, temperature, humidity and wind report from a fixed land station
Introduction
Knowledge of temperature, humidity and wind at levels well above the ground form an essential part of the meteorologist’s basic data.
Variations of wind, temperature and water content occurring well above the ground are as important for weather analysis and forecasting

## Slide 2
Clearly, they cannot be measured by equipment on the ground, but information about the state of the upper air can be obtained in many ways, for example, aircraft reports, but the main one is by observations from balloon-borne equipment.
Balloon observations
These still provide the most valuable source of upper-air data, especially as routine sounding are made simultaneously by an established worldwide network of land-based stations, supplemented by a few observations from ships.

## Slide 3
The standard method of obtaining values of temperature and humidity at upper levels is by use of a balloon carrying a small radio transmitter known as a radiosonde.
Figure 1. Vaisala AS12 autosonde releasing a balloon-borne radiosonde.

## Slide 4
Pressure is measured by an aneroid capsule, temperature by a tiny thermistor or capacitive sensor, and humidity by a small capacitive sensor.
The radiosonde usually contains a GPS or other navigation aid receiver for wind information.
The heights attained by radiosonde balloons vary from about 65000 feet (19.812km) for small balloons to 115000 feet (35.052km) or more for large balloons.
This indicate that from 700km depth of atmosphere the balloon only penetrate a fraction of the earth’s atmosphere.

## Slide 5
Vertical sounding of the atmosphere
During a radiosonde ascent, various measurements of temperature, humidity and pressure at fixed pressure levels and measurements taken at significant pressure levels are sent back to the receiving center in the form of a code and this code is then plotted onto a tephigram.
Below is an example of a coded message from a radiosonde ascent.

## Slide 6
FM 35–XI Ext. TEMP code figure
PART A [Data up to and including 100 mb]
[Section 1] MiMiAA YYGGId IIiii
[Section 2] 99PoPoPo ToToTaoDoDo dodofofofo [Surface Data]
00hhh TTTaDD ddfff 92hhh TTTaDD ddfff 85hhh TTTaDD ddfff 70hhh TTTaDD ddfff 50hhh TTTaDD ddfff 40hhh TTTaDD ddfff 30hhh TTTaDD ddfff 25hhh TTTaDD ddfff 20hhh TTTaDD ddfff 15hhh TTTaDD ddfff 10hhh TTTaDD ddfff
[Standard Isobaric Surfaces]
[Section 3] 88PtPtPt TtTtTatDtDt dtdtftftft [Tropopause Data]
[Section 4] 77PmPmPm dmdmfmfmfm

## Slide 7
FM 35–XI Ext. TEMP code figure
PART A [Data up to and including 100 mb]
MiMiAA YYGGId IIiii
99PoPoPo ToToTaoDoDo dodofofofo 00hhh TTTaDD ddfff 92hhh TTTaDD ddfff 85hhh TTTaDD ddfff 70hhh TTTaDD ddfff 50hhh TTTaDD ddfff 40hhh TTTaDD ddfff 30hhh TTTaDD ddfff 25hhh TTTaDD ddfff 20hhh TTTaDD ddfff 15hhh TTTaDD ddfff 10hhh TTTaDD ddfff
88PtPtPt TtTtTatDtDt dtdtftftft 77PmPmPm dmdmfmfmfm

## Slide 8
TTAA 51231
03808 99996 07819 17005 00057 ///// ///// 92698 03843 20018 85379 00356 20020 70934 04976 22032 50550 19143 27537 40713 29940 27552 30912 44335 27069 25032 54327 28571 20171 61931 29570 15353 54782 27047 10614 54982 25523 88207 62929 29586 77214 29090 42341 31313 48008 82315
TTBB 51238 03808 00996 07819 11995 08018 22990 08021 33980 07625 44969 06823 55948 05650 66915 03042 77875 00108 88867 00717 99859 01314 11855 01318 22851 00741 33845 02469 44840 03873 55831 04276 66817 03873 77816 03673 88786 01674 99734 02174 11667 07976 22618 11572 33607 12765 44601 11910 55548 15310 66517 17343 77462 22339 88455 22934 99441 24728 11398 30141 22377 33131 33327 39535 44308 42926 55267 50935 66244 55723 77226 58933 88219 60729 99207 62929 11200 61932 22194 59957 33187 59762 44185 59964 55174 54774 66171 54777 77160 57381 88143 53383 99120 54383 11113 52783 22100 54982 21212 00996 17005 11984 18514 22973 19018 33951 20517 44871 18521 55852 20019 66834 21022 77731 22530 88716 22033 99679 23029 11605 25034 22519 27036 33469 28042 44411 28053 55354 27056 66348 27061 77309 27570 88291 27071 99288 27069 11261 28065 22214 29090 33207 29586 44201 29573 55193 28547 66189 27048 77186 27053 88181 27559 99178 28054 11172 28039 22169 27032 33165 26034 44159 26040 55150 27547 66143 27033 77137 26031 88116 25535 99111 26538 11100 25523 31313 48008 82315 41414 28472 51515 11892 19022 22800 21025 33600 25034

## Slide 9
TTAA 51231
03808 99996 07819 17005 00057 ///// ///// 92698 03843 20018 85379 00356 20020 70934 04976 22032 50550 19143 27537 40713 29940 27552 30912 44335 27069 25032 54327 28571 20171 61931 29570 15353 54782 27047 10614 54982 25523 88207 62929 29586 77214 29090 42341 31313 48008 82315
MiMiAA YYGGId IIiii
99PoPoPo ToToTaoDoDo dodofofofo 00hhh TTTaDD ddfff 92hhh TTTaDD ddfff 85hhh TTTaDD ddfff 70hhh TTTaDD ddfff 50hhh TTTaDD ddfff 40hhh TTTaDD ddfff 30hhh TTTaDD ddfff 25hhh TTTaDD ddfff 20hhh TTTaDD ddfff 15hhh TTTaDD ddfff 10hhh TTTaDD ddfff
88PtPtPt TtTtTatDtDt dtdtftftft 77PmPmPm dmdmfmfmfm

## Slide 10
As you can see, this message is broken into two sections (TTAA and TTBB). Part A of the code (TTAA) is the values at set pressure levels (1000mb, 925mb, 850mb, 700mb, 500mb, 400mb, 300mb, 250mb, 200mb, 150mb and 100mb.
Also included is tropopause data and maximum wind data) and these levels are mandatory in any upper-air ascent. Part B (TTBB) is for values at ‘significant’ pressure levels.

## Slide 11
Decode of the mandatory levels (TTAA) in the upper air code:
TTAA YYGGI IIiii - Message identification
99PoPoPo ToToTaoDoDo dododofofo - Surface data
00hhh TTTaDD dddff - 1000 mb data
92hhh TTTaDD dddff - 925 mb data
85hhh TTTaDD dddff - 850 mb data
70hhh TTTaDD dddff - 700 mb data
50hhh TTTaDD dddff - 500 mb data
40hhh TTTaDD dddff - 400 mb data
30hhh TTTaDD dddff - 300 mb data
25hhh TTTaDD dddff - 250 mb data
20hhh TTTaDD dddff - 200 mb data
15hhh TTTaDD dddff - 150 mb data
10hhh TTTaDD dddff - 100 mb data
88PtPtPt TtTtTatDtDt dtdtdtftft - Tropopause data
77PmPmPm dmdmdmfmfm - Maximum wind data
31313 - Regional data
Table 1. The Decode of the Upper-Air Code for Part A (TTAA)

## Slide 12
All ascent can be broken down as follows:
Message identification – TTAA
TTAA 51231 03808 99996 07819 17005 00057 ///// ///// 92698 03843 20018 85379 00356 20020 70934 04976 22032 50550 19143 27537 40713 29940 27552 30912 44335 27069 25032 54327 28571 20171 61931 29570 15353 54782 27047 10614 54982 25523 88207 62929 29586 77214 29090 42341 31313 48008 82315
Part A indicator (mandatory levels)

## Slide 13
TTAA 51231 03808 99996 07819 17005 00056 ///// ///// 92698 03843 20018 85379 00356 20020 70934 04976 22032 50550 19143 27537 40713 29940 27552 30912 44335 27069 25032 54327 28571 20171 61931 29570 15353 54782 27047 10614 54982 25523 88207 62929 29586 77214 29090 42341 31313 48008 82315
Message identification – YYGGI (YY: month/date; GG: time of ascent; I: last standard isobaric level that wind data is given)
Day of the month (YY) (51 = 1st) (Day of the month of observation plus 50, e.g. 55 = 5th day of the month)
Time of ascent (GG) (23 = 2300z)
Last reported wind level (I) (1 = 100mb)

## Slide 14
Message identification – IIiii (unique station number )
TTAA 51231 03808 99996 07819 17005 00056 ///// ///// 92698 03843 20018 85379 00356 20020 70934 04976 22032 50550 19143 27537 40713 29940 27552 30912 44335 27069 25032 54327 28571 20171 61931 29570 15353 54782 27047 10614 54982 25523 88207 62929 29586 77214 29090 42341 31313 48008 82315
03 WMO Region indicator and 808 indicates station number

## Slide 15
Surface data – 99PoPoPo (surface pressure)
TTAA 51231 03808 99996 07819 17005 00056 ///// ///// 92698 03843 20018 85379 00356 20020 70934 04976 22032 50550 19143 27537 40713 29940 27552 30912 44335 27069 25032 54327 28571 20171 61931 29570 15353 54782 27047 10614 54982 25523 88207 62929 29586 77214 29090 42341 31313 48008 82315
99 Surface information indicator
996 Surface pressure (PoPoPo) 996mb

## Slide 16
19 Dew-point depression (DoDo) (1.9 °C)
Surface data – ToToTaoDoDo (surface dry-bulb and dew-point temperature)
TTAA 51231 03808 99996 07819 17005 00056 ///// ///// 92698 03843 20018 85379 00356 20020 70934 04976 22032 50550 19143 27537 40713 29940 27552 30912 44335 27069 25032 54327 28571 20171 61931 29570 15353 54782 27047 10614 54982 25523 88207 62929 29586 77214 29090 42341 31313 48008 82315
(Note – in the code, if this figure is an even number (0,2,4,6,8) the value if positive; if the figure is odd (1,3,5,7,9) then the value is negative)
078 Surface air temperature (ToToTao) (7.8 °C)

## Slide 17
Surface data – dododofofo (surface wind direction and speed)
TTAA 51231 03808 99996 07819 17005 00056 ///// ///// 92698 03843 20018 85379 00356 20020 70934 04976 22032 50550 19143 27537 40713 29940 27552 30912 44335 27069 25032 54327 28571 20171 61931 29570 15353 54782 27047 10614 54982 25523 88207 62929 29586 77214 29090 42341 31313 48008 82315
170 is Wind direction (dododo) and 05 is speed (fofo) (170 degrees 05 knots)
Why the unit of wind speed is knots b/c the date of observation is written grater than 50. If the date of observation is written from 1 up to 31 the unit of wind speed will be m/s.

## Slide 18
1000 mb data – 00hhh (height of the 1000 mb level)
TTAA 51231 03808 99996 07819 17005 00056 ///// ///// 92698 03843 20018 85379 00356 20020 70934 04976 22032 50550 19143 27537 40713 29940 27552 30912 44335 27069 25032 54327 28571 20171 61931 29570 15353 54782 27047 10614 54982 25523 88207 62929 29586 77214 29090 42341 31313 48008 82315
00 is 1000mb height indicator
056 is Height of 1000mb level (hhh) (056 = 56 metr

## Slide 19
1000 mb data – TTTaDD (dry-bulb and dewpoint temperature at the 1000mb level)
TTAA 51231 03808 99996 07819 17005 00056 ///// ///// 92698 03843 20018 85379 00356 20020 70934 04976 22032 50550 19143 27537 40713 29940 27552 30912 44335 27069 25032 54327 28571 20171 61931 29570 15353 54782 27047 10614 54982 25523 88207 62929 29586 77214 29090 42341 31313 48008 82315
1000mb dry-bulb temperature and dew-point depression (TTTaDD) (///// = no temperature data recorded for this level)

## Slide 20
1000 mb data – dddff (1000 mb level wind direction and speed)
TTAA 51231 03808 99996 07819 17005 00056 ///// ///// 92698 03843 20018 85379 00356 20020 70934 04976 22032 50550 19143 27537 40713 29940 27552 30912 44335 27069 25032 54327 28571 20171 61931 29570 15353 54782 27047 10614 54982 25523 88207 62929 29586 77214 29090 42341 31313 48008 82315
1000mb wind direction (ddd) and speed (ff) (///// = no wind data recorded for this level)

## Slide 21
925 mb data – TTTaDD (dry-bulb and dewpoint temperature at the 925mb level)
TTAA 51231 03808 99996 07819 17005 00056 ///// ///// 92698 03843 20018 85379 00356 20020 70934 04976 22032 50550 19143 27537 40713 29940 27552 30912 44335 27069 25032 54327 28571 20171 61931 29570 15353 54782 27047 10614 54982 25523 88207 62929 29586 77214 29090 42341 31313 48008 82315
925 mb dry-bulb temperature (TTTa) (038 = 3.8 °C) (Note – in the code, this figure is an even number so the value is positive)
925 mb dew-point depression (DD) (4.3 °C) (3.8 – 4.3 = -0.5 is dew-point temp.)

## Slide 22
925 mb data – dddff (925 mb level wind direction and speed)
TTAA 51231 03808 99996 07819 17005 00056 ///// ///// 92698 03843 20018 85379 00356 20020 70934 04976 22032 50550 19143 27537 40713 29940 27552 30912 44335 27069 25032 54327 28571 20171 61931 29570 15353 54782 27047 10614 54982 25523 88207 62929 29586 77214 29090 42341 31313 48008 82315
1000mb wind direction (ddd) and speed (ff) (200 degrees, 18 knots)

## Slide 23
850 mb data – 85hhh (height of the 850 mb level)
TTAA 51231 03808 99996 07819 17005 00056 ///// ///// 92698 03843 20018 85379 00356 20020 70934 04976 22032 50550 19143 27537 40713 29940 27552 30912 44335 27069 25032 54327 28571 20171 61931 29570 15353 54782 27047 10614 54982 25523 88207 62929 29586 77214 29090 42341 31313 48008 82315
850 mb height indicator (85)
Height of 850 mb level (hhh) (1379 metres) (To convert the height value to metres at the 850 mb level, a leading 1 is necessary (see table below for more details))

## Slide 24
850 mb data – TTTaDD (dry-bulb and dewpoint temperature at the 850mb level)
TTAA 51231 03808 99996 07819 17005 00056 ///// ///// 92698 03843 20018 85379 00356 20020 70934 04976 22032 50550 19143 27537 40713 29940 27552 30912 44335 27069 25032 54327 28571 20171 61931 29570 15353 54782 27047 10614 54982 25523 88207 62929 29586 77214 29090 42341 31313 48008 82315
850 mb dry-bulb temperature (TTTa) (003 = -0.3 °C) (Note – in the code, this figure is an odd number so the value is negative)
850 mb dew-point depression (DD) (56 = -6.3 °C (6.0 °C colder than the dry bulb)) (When the depression is 5.0 °C or less the value is in units and tenths. When the depression is more than 5.0 °C the units and tenths are reported but 50 is added to the total, therefore 56 is 6 whole degrees)

## Slide 25
850 mb data – dddff (850 mb level wind direction and speed)
TTAA 51231 03808 99996 07819 17005 00056 ///// ///// 92698 03843 20018 85379 00356 20020 70934 04976 22032 50550 19143 27537 40713 29940 27552 30912 44335 27069 25032 54327 28571 20171 61931 29570 15353 54782 27047 10614 54982 25523 88207 62929 29586 77214 29090 42341 31313 48008 82315
850mb wind direction (ddd) and speed (ff) (200 degrees, 20 knots)

## Slide 26
Wind speeds greater than 100 knots
Wind direction is reported to the nearest 5 degrees, e.g. 300 = 300 degrees, 095 = 95 degrees). However, sometimes the wind direction appears as either 301 or 306; this indicates either a wind direction of 300 or 305 and speed of 100 knots or more. For example, if we had a wind code of 35110, then the direction would be 350 degrees, and the wind speed would be 110 knots but if the wind code was 35610 then the wind direction would be 355 degrees and the wind speed would be 110 knots.

## Slide 27
Height conversion table
Table 2. Height Conversion Table.

## Slide 28
Tropopause data - 88PtPtPt (Pressure level of the tropopause)
TTAA 51231 03808 99996 07819 17005 00056 ///// ///// 92698 03843 20018 85379 00356 20020 70934 04976 22032 50550 19143 27537 40713 29940 27552 30912 44335 27069 25032 54327 28571 20171 61931 29570 15353 54782 27047 10614 54982 25523 88207 62929 29586 77214 29090 42341 31313 48008 82315
Tropopause height indicator (88)
Pressure level of tropopause (PtPtPt) (207 mb)

## Slide 29
Tropopause data - TtTtTatDtDt (dry-bulb and dewpoint temperature of the tropopause)
TTAA 51231 03808 99996 07819 17005 00056 ///// ///// 92698 03843 20018 85379 00356 20020 70934 04976 22032 50550 19143 27537 40713 29940 27552 30912 44335 27069 25032 54327 28571 20171 61931 29570 15353 54782 27047 10614 54982 25523 88207 62929 29586 77214 29090 42341 31313 48008 82315
Tropopause dry-bulb temperature (TtTtTat) (629 = -62.9 °C) (Note – in the code, this figure is an odd number so the value is negative)
Tropopause dew-point depression (DtDt) (29 = -65.8 °C (2.9 °C colder than the dry bulb))

## Slide 30
Tropopause data - dtdtdtftft (tropopause wind direction and speed)
TTAA 51231 03808 99996 07819 17005 00056 ///// ///// 92698 03843 20018 85379 00356 20020 70934 04976 22032 50550 19143 27537 40713 29940 27552 30912 44335 27069 25032 54327 28571 20171 61931 29570 15353 54782 27047 10614 54982 25523 88207 62929 29586 77214 29090 42341 31313 48008 82315
Tropopause wind direction (ddd) and speed (ff) (295 degrees, 86 knots)

## Slide 31
Maximum wind data - 77PmPmPm (pressure level of the maximum wind)
TTAA 51231 03808 99996 07819 17005 00056 ///// ///// 92698 03843 20018 85379 00356 20020 70934 04976 22032 50550 19143 27537 40713 29940 27552 30912 44335 27069 25032 54327 28571 20171 61931 29570 15353 54782 27047 10614 54982 25523 88207 62929 29586 77214 29090 42341 31313 48008 82315
Maximum wind Indicator (77)
Maximum wind pressure level (214 mb)

## Slide 32
Maximum wind data - dmdmdmfmfm (maximum wind direction and force)
TTAA 51231 03808 99996 07819 17005 00056 ///// ///// 92698 03843 20018 85379 00356 20020 70934 04976 22032 50550 19143 27537 40713 29940 27552 30912 44335 27069 25032 54327 28571 20171 61931 29570 15353 54782 27047 10614 54982 25523 88207 62929 29586 77214 29090 42341 31313 48008 82315
Maximum wind direction (dmdmdm) and speed (fmfm) (290 degrees 90 knots)

## Slide 33
USET01 HAAB 301200
TTAA 80121 63450
99773 23464 09017 00030 ///// ///// 92742 ///// //// 85496 ///// ///// 70169 12461 13510 50589 05780 11532 40761 16586 10531 30970 29985 02506 25097 40381 29517 20246 52174 27530 15426 66762 28514 10664 78163 15530 88101 78363 15526 77999 31313 48008 81146=
Write station level or sfc pressure, temperature, dew-point, wind direction and speed
Write geopotential height of 300, 700, 250 mb pressure level
What is the maximum wind level pressure?
Write down the tropopause level data
Write down the following pressure level data
600mb, 200mb, 500mb and 100mb